## Slide 1: Arduino Tutorial
Building agile, reliable prototypes

## Slide 2
Our focus:
Quick prototyping
Reliable

## Slide 3: Arduino
Microcontroller
Can interface with sensors/SD card:
  General Purpose Input Output (GPIO): switches, turn LED on/off
  analogRead: connect with analog sensors (piezoelectric, audio)
  I2C interface: connect with digital sensors (accel, gyro, inertial motion unit)
  SPI interface: SD card

## Slide 4: Arduino
// the setup function runs once when you press reset or power the board void setup() { // initialize digital pin 13 as an output. pinMode(13, OUTPUT); } // the loop function runs over and over again forever void loop() { digitalWrite(13, HIGH); // turn the LED on (HIGH is the voltage level) delay(1000); // wait for a second digitalWrite(13, LOW); // turn the LED off by making the voltage LOW delay(1000); // wait for a second }
https://github.com/RFduino/RFduino/blob/master/cores/arduino/main.cpp

## Slide 5: GPIO
Useful for capturing switches, or turn on/off LED
Set mode for the pin
  INPUT
  INPUT_PULLUP: if there’s no input, will be HIGH
  OUTPUT: turn on/off LED
Read or write value
pinMode(pin, mode)
digitalRead(pin, value) digitalWrite(pin, value)

## Slide 6: analogRead
Measure voltages
Measure resistance with voltage divider
Scaled depending on the power
  1024 corresponds to Vcc (power source)
  For example: Vcc 3.3V and get value 170. How much is the voltage?

## Slide 7: I2C
Connect with more complicated sensors, such as inertial motion unit (accelerometer, gyroscope)
I2C interface has 4 pins:
  GND and Vcc
  SCL: for clocking
  SDA: for transferring data
Sending and Receiving

## Slide 8: Soldering
Good temperature: 630F
Let soldering joint cool naturally (avoid forming cold joint)
For long-term device, put glue over the soldering joint (after checking that the joint is working well)
Never solder battery wire directly to board (always go through a JST connector)

## Slide 9: Power consumption
Do not measure it directly (let the battery run out)
  Waste of time
  Cannot be exact (depending on the battery)
Instead measure the current consumed (using power supply)
  Can quickly iterate through different versions of firmware
  Typical battery capacity is 1000mAh.
  Divide battery capacity by current

## Slide 10: Power consumption
Example:
  RFduino when sleeping: 10mA
  Read sensor: 11mA at 20Hz, and sensor reading took 1ms.
  Battery: 350mAh
How long can device last?

## Slide 11: Resource
MG22: 24/7 electronic labs. Access with your WildCard. If you do not have access, contact root@eecs.northwestern.edu and cc TA.
Rapid Prototyping lab: print high quality 3D parts.